## Slide 1: Racing in Hyperspace: Closing Hyper-Threading Side Channels on SGX with Contrived Data Race
Guoxing Chen1* & Wenhao Wang2,3*, Tianyu Chen2, Sanchuan Chen1,
Yinqian Zhang1, XiaoFeng Wang2, Ten-Hwang Lai1, Dongdai Lin3
(*co-first authors)
1The Ohio State University,
2Indiana University Bloomington,
3Institute of Information Engineering, CAS

## Slide 2: Intel SGX
Untrusted application
Untrusted OS
Enclave
Code and data
Side channels

## Slide 3: Side channels
Physical core
Enclave code
Attack code
Caches
BPUs
Asynchronous Enclave eXit (AEX)
AEX-detection based mitigations: T-SGX, Déjà Vu
Side channels enabled or assisted by Hyper-Threading
[1] Shih et al, “T-SGX: Eradicating controlled-channel attacks against enclave programs,” NDSS, 2017
[2] Chen et al, “Detecting privileged side-channel attacks in shielded execution with Déjà Vu,” AsiaCCS, 2017

## Slide 4: Hyper-Threading
Caches
BPUs
TLBs
Intel’s proprietary implementation of simultaneous multithreading (SMT)

## Slide 5: Hyper-Threading enabled side channels
Side Channel | Shared | Cleansed at AEX | HT only
Store Buffers[1][2] | No | N/A | Yes
FPUs | Yes | N/A | Yes
TLBs | Yes | Flushed | Yes
Caches | Yes | Not flushed | No
BPUs | Yes | Not flushed | No
[1] Moghimi et al, “MemJam: A false dependency attack against constant-time crypto implementations,” arXiv, 2017
[2] Sullivan et al, “Microarchitectural minefields: 4k-aliasing covert channel and multi-tenant detection in IaaS clouds,” NDSS, 2018

## Slide 6: Hyper-Threading assisted side channels
Hyper-Threading helps reduce AEXs
  Sneaky Page Monitoring assisted by Hyper-Threading[1]
Invalidate Transactional Synchronization Extensions (TSX) based cache side-channel protection[2]
[1] Wang et al, “Leaky cauldron on the dark land: Understanding memory side-channel hazards in SGX,” CCS, 2017
[2] Gruss et al, “Strong and efficient cache side-channel protection using hardware transactional memory,” USENIX Security, 2017

## Slide 7: Research goals
Close all these Hyper-Threading enabled or assisted side channels
Detect AEX-based side channel attacks

## Slide 8: Challenges
Simply disabling Hyper-Threading
  No effective way to verify: cpuid, rdtscp and rdpid are not supported in enclave mode
Remote attestation
  Does not contain information about Hyper-Threading
Create a shadow thread from the enclave program to occupy the other hyper-thread
  How to reliably verify the physical-core co-location?

## Slide 9: HyperRace overview
Physical core
Physical core
Protected thread
Shadow thread
Frequently check AEX
AEX detected!
Context switches trigger AEXs
Co-location test
Terminate if fail
Contrived data race
Co-location test

## Slide 10: Contrived data race: an illustrating example
Two threads operate on the same shared variable ν:
  Protected thread loops:
    Writes 0 to ν
    Waits for 10 cycles
    Reads ν
  Shadow thread loops:
    Writes 1 to ν
Physical core
Protected thread
Shadow thread
L1 cache
Protected thread reads ν=1 with a high probability
Enclave data: v
Untrusted OS

## Slide 11: Contrived data race: an illustrating example
Protected thread reads ν=1 with a low probability
Physical core
Shadow thread
Untrusted thread
L1 cache
Physical core
Cache coherence protocol
Protected thread
Untrusted thread
L1 cache
(latency ~ 190 cycles on Skylake)

## Slide 12: Contrived data race
Communication time:
Execution time:
When co-located, communication time < execution time
When not co-located, communication time > execution time
Physical core
Protected thread
Shadow thread
L1 cache
Physical core
Protected thread
Untrusted thread
L1 cache
Physical core
Shadow thread
Untrusted thread
L1 cache
write
read

## Slide 13: A refined data-race design
Physical core
Protected thread
Shadow thread
L1 cache
Both threads observe data races with high probability
Enclave data: v
Untrusted OS

## Slide 14: A refined data-race design
read
write
read
write
read
write
read
write
Protected thread
Shadow thread
When co-located, communication time < execution time
Each thread read the value written by the other thread with very high probability.
Communication time

## Slide 15: A refined data-race design
Physical core
Protected thread
Untrusted thread
L1 cache
At least one observe data races with low probability
Physical core
Shadow thread
Untrusted thread
L1 cache

## Slide 16: A refined data-race design
read
write
read
write
read
write
read
write
Protected thread
Shadow thread
When not co-located, communication time > execution time
Each thread read the value written by the other thread with very low probability.
Communication time

## Slide 17: Co-Location Test via Hypothesis Testing

## Slide 18: Co-Location Test code

## Slide 19: Security requirements
Necessary conditions to pass the co-location tests:
  1) communication time < execution time
  2) execution time for both threads should be roughly the same
Theoretical model:
LD
ST
LD
ST
LD
ST
LD
ST
Protected thread
Shadow thread
LD
ST

## Slide 20: Threat model
Physical core
Physical core
Shadow thread
Protected thread
Attack code
L1 cache
Attack code
L1 cache
Try to pass the co-location test by
  Flushing cache
  Changing CPU frequency
  Disabling caching
  Disabling caching + changing CPU frequency
  ……

## Slide 21: Security analysis
Theoretical model
Latency of cache eviction
Latency of cross-core communication
Effects of CPU frequency changes
Effects of disabling caching
The adversary cannot meet both security requirements simultaneously

## Slide 22: Implementation
if (aex_detected()) {
co_location_test();
}
if (aex_detected()) {
co_location_test();
}
if (aex_detected()) {
co_location_test();
}
Every q
instructions
Original code
Instrumented code
LLVM
AEX detection via monitoring the SSA [1].
[1] Gruss et al, “Strong and efficient cache side-channel protection using hardware transactional memory,” in USENIX Security, 2017.
Shadow thread code
protected thread code
HyperRace library

## Slide 23: Performance
Runtime overhead:
  AEX detections
  Co-location tests
Memory overhead:
  Increased code size
AEX detection
Co-location test
Enclave code
AEX detected!
AEX detected!

## Slide 24: Performance
Runtime overhead due to AEX detection (nbench)
Geometric mean = 101.8% when q = 5.

## Slide 25: Performance
Runtime overhead due to co-location test (nbench) with q = 20
Geometric mean = 16.6% when 1000 AEXs per sec.

## Slide 26: Performance
 | Original | q=20 | q=15 | q=10 | q=5
Bytes | 207,904 | 242,464 | 246,048 | 257,320 | 286,448
Overhead | - | 16.6% | 18.3% | 23.7% | 37.7%
Memory overhead (nbench)

## Slide 27: Discussion and conclusion
We designed and implemented a novel co-location technique to close the Hyper-Threading side channels
A bigger lesson: hardware design is performance oriented, but how about their security implications? what can we do if it is vulnerable?
  We show that a software approach could mitigate the threat
  A composition of software solution and hardware feature might help strike a better balance between security and performance